Week5 Lab1: mux_2x1
module mux_2x1_beh(m_out, A, B, select);
output m_out;
input A, B, select;
reg m_out;

always@ (A or B or select)
if(select == 1) m_out = A;
else m_out = B;

endmodule

Week5 Lab2: mux_4x1
module mux_4x1_beh(m_out, in_0, in_1, in_2, in_3, select);
output m_out;
input in_0, in_1, in_2, in_3;
input [1:0]select;
reg m_out;

always @(in_0, in_1, in_2, in_3, select)
case(select)
2'b00: m_out = in_0;
2'b01: m_out = in_1;
2'b10: m_out = in_2;
2'b11: m_out = in_3;
endcase

endmodule

Week5 Lab3: t_mux_4x1
module t_mux_4x1_beh;
wire t_mux_out;
reg t_0, t_1, t_2, t_3;
reg [1:0]t_select;
parameter stop_time = 100;

mux_4x1_beh M1(t_mux_out, t_0, t_1, t_2, t_3, t_select);
initial #stop_time $finish;

initial begin
t_select = 00; t_0 = 0; t_1 = 1; t_2 = 1; t_3 = 1;
#10 t_select = 00; t_0 = 1; t_1 = 0; t_2 = 0; t_3 = 0;
#10 t_select = 01; t_0 = 1; t_1 = 0; t_2 = 0; t_3 = 0;
#10 t_select = 01; t_0 = 0; t_1 = 1; t_2 = 0; t_3 = 0;
#10 t_select = 10; t_0 = 0; t_1 = 1; t_2 = 0; t_3 = 0;
#10 t_select = 10; t_0 = 0; t_1 = 0; t_2 = 1; t_3 = 0;
#10 t_select = 11; t_0 = 0; t_1 = 0; t_2 = 1; t_3 = 0;
#10 t_select = 11; t_0 = 0; t_1 = 0; t_2 = 0; t_3 = 1;
end
initial begin
$monitor("time=", $time, ", select=%b, in_0=%b, in_1=%b, in_2=%b, in_3=%b, m_out=%b", t_select, t_0, t_1, t_2, t_3, t_mux_out);
end
endmodule

module mux_4x1_beh(m_out, in_0, in_1, in_2, in_3, select);
output m_out;
input in_0, in_1, in_2, in_3;
input [1:0]select;
reg m_out;

always @(in_0, in_1, in_2, in_3, select)
case(select)
2'b00: m_out = in_0;
2'b01: m_out = in_1;
2'b10: m_out = in_2;
2'b11: m_out = in_3;
endcase

endmodule

Week5 Lab4: t_full_add
module t_full_add;
wire T1, T2;
reg [2:0]D;

full_adder F1(T1, T2, D);
initial
begin
D = 3'b000;
repeat(7)#10 D = D + 1'b1;
end
initial begin
$monitor("time = ",$time,",ABC=%b F1=%b F2=%b", D,T1,T2);
end
endmodule

module full_adder
(
output reg F1, F2,
input [2:0]D
);
always @(D)
case(D)
3'b000: begin F1 = 1'b0; F2 = 1'b0; end
3'b001: begin F1 = 1'b1; F2 = 1'b0; end
3'b010: begin F1 = 1'b1; F2 = 1'b0; end
3'b011: begin F1 = 1'b0; F2 = 1'b1; end
3'b100: begin F1 = 1'b1; F2 = 1'b0; end
3'b101: begin F1 = 1'b0; F2 = 1'b1; end
3'b110: begin F1 = 1'b0; F2 = 1'b1; end
3'b111: begin F1 = 1'b1; F2 = 1'b1; end
endcase

endmodule

Week6 Lab1: D_FF
module D_FF(Q, D, clk);
output Q;
input D, clk;
reg Q;

always@(posedge clk) // 0->1
Q = D;

endmodule
Week6 Lab2: JK_FF
module JK_FF(input j, k, clk, output reg Q, output Q_b);
assign Q_b = ~Q;
always@(posedge clk)
case({j,k})
2'b00: Q = Q;
2'b01: Q = 0;
2'b10: Q = 1;
2'b11: Q = ~Q;
endcase
endmodule

Week6 Lab3: Mealy_Zero_Detector
module Mealy_Zero_Detector( output reg y_out, input x_in, clk, reset);
reg [1:0]state, next_state;
parameter S0 = 2'b00, S1 = 2'b01, S2 = 2'b10, S3 = 2'b11;

always@(posedge clk, negedge reset)
if(!reset) state = S0;
else state = next_state;
always@(state, x_in)
case(state)
S0: if(x_in) next_state =S1; else next_state =S0;
S1: if(x_in) next_state =S3; else next_state =S0;
S2: if(~x_in) next_state =S0; else next_state =S2;
S3: if(x_in) next_state =S2; else next_state =S0;
endcase
always@(state, x_in)
case(state)
S0: y_out = 0;
S1,S2,S3: y_out = ~x_in;
endcase

endmodule

module t_Mealy_Zero_Detector;
wire t_y_out;
reg t_x_in, t_clk, t_reset;
Mealy_Zero_Detector M1(t_y_out, t_x_in, t_clk, t_reset);
initial#200 $finish;
initial begin t_clk = 0; forever#5 t_clk = ~t_clk; end

initial fork
t_reset = 0;
#2 t_reset = 1;
#87 t_reset = 0;
#89 t_reset = 1;
#10 t_x_in = 1;
#30 t_x_in = 0;
#40 t_x_in = 1;
#50 t_x_in = 0;
#52 t_x_in = 1;
#54 t_x_in = 0;
#80 t_x_in = 1;
#100 t_x_in = 0;
#120 t_x_in = 1;
join
endmodule

Week6 Lab4: Moore_Model
module Moore_Model(
output[1:0] y_out,
input x_in, clock, reset
);
reg[1:0] state;
parameter S0 = 2'b00, S1 = 2'b01, S2 = 2'b10, S3 = 2'b11;
always @(posedge clock, negedge reset)
if(!reset) state = S0;
else
case(state)
S0: if(~x_in) state = S1;
else state = S0;
S1: if(x_in) state = S2;
else state = S3;
S2: if(~x_in) state = S3;
else state = S2;
S3: if(~x_in) state = S0;
else state = S3;
endcase
assign y_out = state;
endmodule

module t_Moore_Model;
wire[1:0] t_y_out;
reg t_x_in, t_clock, t_reset;

Moore_Model M0(t_y_out, t_x_in, t_clock, t_reset);

initial #200 $finish;
initial begin
t_clock = 0;
forever #5 t_clock = ~t_clock;
end
initial fork
t_reset = 0;
#2 t_reset = 1;
#87 t_reset = 0;
#89 t_reset = 1;
#10 t_x_in = 1;
#30 t_x_in = 0;
#40 t_x_in = 1;
#50 t_x_in = 0;
#52 t_x_in = 1;
#54 t_x_in = 0;
#80 t_x_in = 1;
#100 t_x_in = 0;
#120 t_x_in = 1;
join
endmodule